## Slide 1: Interaction and Perception
Notes: Krish and Maglio (1994) -epistemic actions = activities that uncover new information.
Otherwise, just clutter.

## Slide 2: Taxonomy of Infoviz Tasks
Overview: See overall patterns, trends
Zoom: See subset
Filter: See subset based on attributes
Details on demand: See more about specific object
Relate: See relationships, compare values
History: Keep track of actions and insights
Extract: Mark and capture specific data

## Slide 3: Visual Information Seeking Mantra
Overview first,
zoom and filter,
details on demand.
—Ben Shneiderman

## Slide 4: Three Types of Feedback Loops
Data selection and manipulation
  Most important for interactive visualization
Exploration and navigation
Problem solving

## Slide 5
Reaction times
Daily Cal
Notes: Photo: http://www.dailycal.org/2015/02/24/no-14-cal-mens-tennis-falls-stanford-defeats-gaels-gauchos/

## Slide 6: Simple Reaction Times
Optimal (finger at the ready)
~130 ms (Kohlberg, 1971)
Infrequent (still at the ready)
Up to 700 ms (Warrick et al., 1964)
Notes: = no choice

## Slide 7: Choice Reaction Times
Hick-Hyman law:
Reaction Time = a + blog2(C)
Where C = number of choices,
and a and b are constants.
log2(C) is information processed by humans in bits.

## Slide 8: Choice Reaction Times
Hick-Hyman law:
Dealing with choice is expensive

## Slide 9
Minimize visual noise
Notes: Impacts on reaction time: visual noise, degree of accuracy.

## Slide 10
@ftrain

## Slide 11
System Response Times

## Slide 12: Three Thresholds
0.1 s for visual continuity, feels like real time:
animations, sliders
1 s for reasonable system response:
pause in conversation
10 s for process expected to be slow:
cognitive response
threshold for suspecting system is broken

## Slide 13
Diagram source: Ware, 2010

## Slide 14: Fitts’s Law
Selection time = a + b log2(D/W + 1)
D = distance to target
W = width of target
log2(D/W + 1) is index of difficulty (in bits)
1/b = index of performance (in bits/s), roughly constant, typically ~4

## Slide 15: Fitts’s Law
Time increases as distance to target increases
Time increases as width of target gets smaller
Notes: Paul Fitts

## Slide 16: Fitts’s Law
Keep controls that you want users to easily move between near each other.
Make click targets large.
Keep controls that users should use rarely away from commonly used controls.

## Slide 17: Fitts’s Law
Submit
Delete All

## Slide 18: Visual Information Seeking Mantra
Overview first, zoom and filter, details on demand.
Overview first, zoom and filter, details on demand.
Overview first, zoom and filter, details on demand.